## Slide 1: Wireless Data Transmission
Lab 1 & 2
Jonathan Woong
CS M117 – Discussion 1B – Summer 2017
July 18, 2017

## Slide 2: Abstract (Goals)
Lab 1
  Develop a basic understanding of wireless throughput by analyzing UDP and TCP connections under multiple scenarios
  Experience potential instability of TCP under certain circumstances
  Become familiar with network performance measurement tools
  Measure the relationship between communication distance and data transmission rates/signal strength
Lab 2
  Measure the relationship between communication distance and Bit Error Rate (BER)
  Measure the effects of one-to-many Bluetooth connections on multiple devices
  Measure the interference of Bluetooth devices
  Measure the interference and fairness between Bluetooth and IEEE 802.11 devices

## Slide 3: Theory
Lab 1A
  UDP iperf client sends constant bit rate stream to server
  UDP iperf server reports datagram losses and throughput
  TCP iperf client sends as much data as possible for a fixed time period
  TCP iperf server reports throughput
  Expect UDP (No ACK) to be faster than TCP (ACK)
Lab 1B
  Expect microwave interference to reduce WiFi throughput due to shared frequency

## Slide 4: Theory
Lab 2A
  Expected data rates: DH1 < DH3 < DH5
  Expect data rate to decrease as distance increases
Lab 2B
  Expect data rate to decrease as number of slaves increases
Lab 2C
  Expect data rate to decrease with crossing connections due to interference
Lab 2D
  Expect Bluetooth throughput to be less than WiFi throughput

## Slide 5: Lab 1A Results – TCP and UDP Throughput vs. Signal Strength
Location | Approx. Distance from Access Point (feet) | Signal Strength (dBm) | Noise Power (dBm) | SNR (dB) | UDP Data Rate (Kbps) | TCP Data Rate (Kbps) | Observations
Wall Across 3704 Entry | 30 ft | -64 | -83 | 19 | 15,800 | 18,400 | 
Next to 3428 Suite Main Entry | 60 ft | -71 | -82 | 11 | 5,470 | 1,240 | Did not receive ACK of last datagram after 10 tries
Next to 3424 Entry | 90 | -81 | -87 | 6 | 1,100 | 892 | 1 datagram received out of order

## Slide 6: Lab 1A Results – Diagrams
Chart: Distance vs. Signal Strength
| 30.0 | 60.0 | 90.0
 | -64 | -71 | -81
Chart: Distance vs. Signal-to-Noise Ratio
| 30.0 | 60.0 | 90.0
 | 19 | 11 | 6
Chart: Signal-to-Noise Ratio vs. UDP Throughput
| 19.0 | 11.0 | 6.0
 | 15800 | 5470 | 1100
Chart: Signal-to-Noise Ratio vs. TCP Throughput
| 19.0 | 11.0 | 6.0
 | 18400 | 1240 | 892

## Slide 7: Lab 1B Results – Noise & Throughput with Microwave Oven
Microwave Oven Level | Signal Strength (dBm) | Noise Power (dBm) | UDP Data Rate (Kbps) | TCP Data Rate (Kbps) | Spectrum Analyzer Display Observation (GHz) | Observations
Off | -27 | -80 | 121 | 21,000 | 0 | None
High | -30 | -83 | 46.6 | 18,200 | 30 | 1 datagram received out of order
Medium High | -27 | -80 | 87.1 | 17,300 | 25 | 1 datagram received out of order
Medium | -29 | -80 | 70.6 | 15,000 | 25 | 1 datagram received out of order
Defrost | -31 | -80 | 76.2 | 20,800 | 25 | None
Warm | -27 | -81 | 81.1 | 18,700 | 20 | 1 datagram received out of order

## Slide 8: Lab 1B Results -- Diagrams
Chart: Microwave Strength vs. UDP Throughput
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0
 | 121 | 81.1 | 76.2 | 70.6 | 87.1 | 46.6
Chart: Microwave Level vs. TCP Throughput
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0
 | 21000 | 18700 | 20800 | 15000 | 17300 | 18200

## Slide 9: Lab 2A & 2B Results – Data Throughput vs. Distance & Data Throughput vs. # of Slaves
Distance (ft) | Packet Type | Data Rate (Kbps) | Observations
10 | DH1 | 55 | Consistent
 | DH3 | 180 | “
 | DH5 | 240 | Inconsistent
15 | DH1 | 45 | Consistent
 | DH3 | 120 | “
 | DH5 | 210 | Inconsistent
30 | DH1 | 16 | Consistent
 | DH3 | 70 | “
 | DH5 | 80 | Inconsistent
Number of Slaves | Packet Type | Data Rate (Kbps) | Observations
1 | DH1 | 60 | Base
 | DH3 | 195 | “
 | DH5 | 260 | “
2 | DH1 | 15 | 4x smaller
 | DH3 | 50 | “
 | DH5 | 65 | “
3 | DH1 | 8 | 8x smaller
 | DH3 | 25 | “
 | DH5 | 40 | “

## Slide 10: Lab 2C & 2D Results – Fairness of Bluetooth & Fairness between Bluetooth and 802.11b TCP
Case | Pair Data Rate (Kbps) | Observations
Before Interference | 266.56 | None
3 connections crossing | 175 | Many tries to establish connection
 | 260 | “
 | 100 | “
 | Data Rate (Kbps) | Observations
Bluetooth Throughput | 266.56 | None
802.11b TCP Throughput | 20,000 | None

## Slide 11: Lab 2A & 2B – Diagrams
Chart: Data Throughput vs. Distance
| 10.0 | 15.0 | 30.0
DH1 | 55 | 45 | 16
DH3 | 180 | 120 | 70
DH5 | 240 | 210 | 80
Chart: # of Slaves vs. Data Throughput
| 1.0 | 2.0 | 3.0
DH3 | 195 | 50 | 25
DH1 | 60 | 15 | 8
DH5 | 260 | 65 | 40

## Slide 12: Discussion
Lab 1A
  The decrease in UDP throughput is fairly linear with decrease in SNR
  The decrease in TCP is not very linear with decrease in SNR
  TCP throughput decreased faster than that UDP throughput
Lab 1B
  UDP throughput is significantly lower than TCP throughput with Microwave Off
  UDP throughput is significantly lower than TCP throughput with Microwave On
  UDP throughput decreases more than TCP throughput with Microwave On
Lab 2A
  Data rate relationship: DH1 < DH3 < DH5
  Data rate decreases almost linearly as distance increases
Lab 2B
  Data rate relationship: DH1 < DH3 < DH5
  Data rate decreases almost exponentially as number of slaves increases
Lab 2C
  Data rates for 3 connections crossing is inconsistent
  Data rates for 3 connections crossing is expected to decrease (maybe error was made)
Lab 2D
  Bluetooth and WiFi fairness accurate: WiFi throughput is significantly higher than Bluetooth

## Slide 13: Conclusion
For both TCP, UDP, and Bluetooth, throughput will decrease as distance, number of nodes, and interference increases
Bluetooth transmission speeds are always much lower than WiFi
iperf is a tool for performing measurements on network parameters
Results were fairly consistent with expectations